## Slide 1: OCP Caliptra Workshop: Attestation Architecture
Fabrizio D’Amato (AMD)
Jeff Andersen (Google)

## Slide 2: Device Attestation with Caliptra
Agenda:
Attestations Framework and Caliptra Role
How DICE, DPE, SPDM , CoRIM work together
RATS Architecture and claim mapping

## Slide 3: Attestation Framework
Reference Value Provider
Attester
Verifier
Relying Party
Reference Values
Endorser
Endorsements
Appraisal Results
Caliptra Integrated Device
3rd Party Auditors
Evidence
OCP EAT
CoRIM
(ref val)
CoRIM (SFR)
End Customer
Device Vendor
EAT = Entity Attestation Token
CoRIM = Concise Reference Integrity Manifest
EAR = EAT Attestation Result
SFR = Short Form Report
TCBInfo
(DICE/
DPE)
EAR

## Slide 4: Identity vs Inventory Attestation
Identity Attestation (DICE + DPE):
Purpose: "Who am I and am I authentic?"
Proves: Device/component identity and integrity
Mechanism: Certificate chains with measurements
Example: "I am legitimate SPDM Responder"
Inventory Attestation (SPDM):
Purpose: "What components are installed?"
Reports: Complete system inventory
Mechanism: Enumeration + measurement collection
Example: "I contain: Bootloader, OS, APP XYZ"
Identity (DICE+DPE) proves the inventory reporter is authentic
↓
Inventory (SPDM) can be trusted because reporter is verified

## Slide 5: DICE VS DPE
Caliptra RoT FW Attestation - DICE
Purpose: “is Caliptra running trusted firmware?”
Proves: Caliptra booted with Authentic firmware and secure fuse settings
Mechanism: Certificate chains with measurements
Example: "I am legitimate Caliptra firmware "
Inventory Application Attestation - DPE
Purpose: “is the SPDM Responder Authentic ?”
Proves: integrity of the Attester Application
Mechanism: Certificate chains with measurements
Example: "I am legitimate SPDM Responder "
DICE proves that Caliptra is running authentic firmware and fuse configuration
      ↓
DPE can be trusted to attest to the SPDM Responder

## Slide 6: Attester Composition
An Attester is composed of:
Multiple Target Environments, components like firmware and HW configs.
Single Attesting Environment, which:
Collects Target Environments claims
Signs evidence
Target Environment Claims:
Identification (Environment Map)
Uniquely Identifiable by triple: Vendor, Model, and ClassID
- Properties (Measurement Map)
Digest, SVN, FWVersion, Flags, etc
Attesting Environment
Target
Env 0
Target
Env 1
Target
Env 2
Device Attester
{
Vendor
Model
ClassID
}
{
Digest
SVN
…
}
{
Vendor
Model
ClassID
}
{
Digest
SVN
…
}
{
Vendor
Model
ClassID
}
{
Digest
SVN
…
}
Environment Map
Measurement Map
Definition from Remote ATtestation ProcedureS (RATS)
Notes: This slide explains the structure of attestation environments, focusing on the role of Caliptra as the attesting environment that collects and signs data from various target components. It highlights the importance of Target Environments being measurable parts such as firmware or hardware configurations. The universal identification triple ensures consistency across different attestation artifacts, facilitating automated verification.

## Slide 7: Mapping TCBInfo with Vendor CoRIM

## Slide 8: Mapping TCBInfo with CoRIM SAFE

## Slide 9: Journey Measurements Claims
Caliptra integrated SoC may support hitless updates.
Journey Measurements records each component firmware state
  Journey Measurement = HEM (Journey Measurement -1 | Current Measurement)
  *HEM = Hash Extended Measurement
Journey Measurements are reported as IntegrityRegisters[0] in the TCBInfo
Fwids
Svn
Flags
IntegrityRegisters
TCBInfo
Verifier
Where do I find reference measurement for IntegrityRegisters ?

## Slide 10: Journey Measurement: Cold Boot
The initial IntegrityRegisters reference value is included as a claim in the CoRIM
Fwids
Svn
Flags
IntegrityRegisters
TCBInfo
Digests
Svn
Flags
IntegrityRegisters
Cold Boot
Claims Match?
CoRIM
(Measurement Map)
Device
Verifier
Reference Value Provider

## Slide 11: Journey Measurement: Hitless Update
Fwids
Svn
Flags
IntegrityRegisters
TCBInfo
Digest A
Svn
Flags
IntegrityRegisters
CoRIM
(Measurement Map)
Device
Verifier
Reference Value Provider
Digest B
Svn
Flags
IntegrityRegisters
Digest A
Digest B
Event Log
1. Check if Digests Matches w/ CoRIM Reference Value

## Slide 12: Journey Measurement: Hitless Update
Fwids
Svn
Flags
IntegrityRegisters
TCBInfo
Digest A
Svn
Flags
IntegrityRegisters
CoRIM
(Measurement Map)
Device
Verifier
Reference Value Provider
Digest B
Svn
Flags
IntegrityRegisters
Digest A
Digest B
Event Log
RefVal = (0 | A | B)
2. Calculate Reference Value from Event Log

## Slide 13: Journey Measurement: Hitless Update
Fwids
Svn
Flags
IntegrityRegisters
TCBInfo
Digest A
Svn
Flags
IntegrityRegisters
CoRIM
(Measurement Map)
Device
Verifier
Reference Value Provider
Digest B
Svn
Flags
IntegrityRegisters
Digest A
Digest B
Event Log
RefVal = (0 | A | B)
3. Compare Reference Value against Evidence

## Slide 14: Call To Action
Let’s standardize attestation protocol / formats and improve interoperability
Review the CoRIM Draft and RATS Attestation Architecture
Review the IETF Evidence Transformation Draft
Review the OCP EAT Profile Draft

## Slide 15: Backup

## Slide 16: Journey Measurement: Hitless Update
CoRIM can`t have a reference value for the IntegrityRegisters after Hitless Update
Appraisal Policy Steps:
The Verifier receives an event-log, which includes the ordered lists of digest updated since cold boot
  Component (Vendor, Model, ClassID):
    Digest A
    Digest B
    Digest N
The Verifier corroborates Digests in the event-log against CoRIM(s)
3. The Verifier calculates the Reference Value for the IntegrityRegisters
  - RefVal_IntegrityRegisters = SHA384(DigestA | DigestB | DigestB)
4. The Verifier corroborates the calculated Reference Value against the IntegrityRegisters from TCBInfo

## Slide 17: Appraisal Policy of Caliptra TCBInfo
1. Evidence Collection: Relying Party collects Evidence from the Attester containing multiple Target Environments (TEs)
2. Data Provision: Relying Party provides Evidence and Event Logs (if available) to Verifier, where each event log is specific to an individual TE (e.g., a firmware component)
3. TE Processing: For each TE in the Evidence, the verifier looks for a reference value in the CoRIM
4. Integrity-Registers Verification: For the "integrity-registers" claim, if there's no match in CoRIM, the verifier:
  Checks for an Event Log associated to the TE
  If present, checks for a match to each Digest in the Event Log in CoRIM
  If pass, cumulates all digests in the Event Log and checks for match with integrity-registers
5. Endorsement Processing: The Verifier looks for any endorsement associated to the TE (e.g., SAFE) and augments each TE with the
6. Endorsement
Result Return: Return Pass/Fail and TE Augmentation to Relying Party
Backup